Annex IX

MEASURES FOR THE CONTROL OF EMISSIONS OF AMMONIA FROM AGRICULTURAL SOURCES

E. Outside manure storage

8. Within one year from the date of entry into force of the amended Protocol, a Party shall use for new slurry stores on all farms, low-emission storage systems or techniques that have been shown to reduce emissions by at least 60% (ambition level B), or more, compared to the reference (as listed in the guidance document referred to in paragraph 6), or other systems or techniques with a demonstrably equivalent efficiency. A higher reduction efficiency of 80 % may be achieved through the use of rigid lids, roofs, tents or storage bags (ambition level A).  A lower ambition (level C), may be appropriate in the case of small farms (< 15 livestock units?), through the exclusion of the store cover requirement, where 40% reduction in emissions may be achieved through natural crusting or floating covers.

9. For existing slurry stores, on all farms, a Party shall achieve emission reductions of at least 40% (ambition levels A and B) (e.g. via the formation of a natural crust. For pig slurry storage, formation of a crust can be facilitated through the addition of chopped straw, except in the case of very large lagoons). The timescale for the application of these measures shall be: on ratification. For ambition level C, whilst it should be possible for all farms, except in the case of very large lagoons, to allow the formation of natural crusts on existing slurry stores without delay, additional time (until 31 December 2017) should be allowed for farms to adopt the use of chopped straw or floating plastic foil where natural crusts do not form [Insert: , as far as the Party considers this feasible.].