Influence of measures for the control of ammonia emissions in the profitability of pig farms in Spain

Lead author: Carlos Pineiroa

Contributing authors: Gema Montalvob, Mariano Herreroc, Manuel Bigeriegod

- PigCHAMP Pro Europa

- Tragsega

- Feaspor

- Spanish Ministry of the Environment and Rural and Marine Affairs

# Executive Summary

The objective of this study is to determine what is the most cost-effective methods for reducing ammonia emission in the pig sector, that is to say, to select the more efficacy phases and techniques to abate ammonia emissions.

With this aim, a calculation on cost of ammonia reduction techniques under Spanish conditions, for the pig sector, and the influence of its application in the profitability margins is presented.

The calculation was carried out according to the methodology set out in BREF, 2003. The costs were calculated for feeding techniques, animal housing, slurry storage and spreading techniques (Options A, B or C of Annex IX). Units used for assessing costs were € per place (or m3) per year (as BREF, 2003), € per kg NH3 (as GAINS) and € per kg pig produced, because in the pig sector it is more easily understood, and it is easier to calculate the cost for all production process.

The study concludes that economic resources to improve environmental conditions in pig farm are limited because the small profitability of livestock sector in Europe. If Administration demands hard measures for the control of emissions, profitability will disappear. Instead of reducing ammonia emissions, these will be transferred to other world areas under an less restrictive environmental legislation.

Nutritional and land application strategies are the most effective techniques, while housing strategies in gestating, lactating or weaners rooms increase significantly cost production and the reduction in ammonia emissions is negligible.

It is indispensable that the environmental demands do not finish with the profitability of livestock sector. Because this, to calculate total cost of techniques implemented is so important as to know the total environmental benefit. Current proposed measures for the control of ammonia emissions from agricultural sources will be finished take into account the profitability of affected farms.

# Introduction

The purpose of this report is to provide information on the additional costs incurred by farmers for measures to abate ammonia emissions from livestock systems.

The information is intended to be used to contribute to the calculation of the most efficient methods of reducing ammonia emissions from European farms.

The costs shown in this report relate to the extra costs for farmers with production and management systems that are typical for the country.  For each abatement technique, the typical (or reference system) is described in addition to the changes that are needed in order to reduce emissions.  Information about extra costs is compared with profitability margins in the last years to pig sector, to evaluate the economic capacity of farmers to support option A, B or C of Annex IX.

Considerable advice and assistance has been provided by a number of technical experts, machinery and building manufacturers and suppliers, and by farmers and contractors during the course of the preparation of these costing.

The calculations have been carried out according to the methodology set out in the IPPC Reference Document on Best Available Techniques for Intensive Rearing of Poultry and Pigs, 2003.

The information has been prepared at the request of Spanish Ministry of the Environment and Rural and Marine Affairs.

# Methodology

## Overview

The calculation of unit cost requires a clear understanding of:

- The proposed techniques to be introduced to reduce emissions

- The whole range of systems of production and management that are found on affected farms in the country concerned.

- The impact that the introduction of the technique will have on particular farm production and management systems in both physical and financial terms.

## Categories of techniques

Techniques applicable to the intensive livestock sector of the agricultural industry may be described by one of the following categories:

- Feed

- Housing

- Manure and slurry storage

- Treatment of manure

- Application of manure to land

## Calculation of unit costs

Unit costs are the annual increase in costs that a typical farmer will bear as a result of introducing a technique. The general approach to the calculation of unit costs is as follows:

- Define the physical and husbandry changes resulting from implementation of the abatement technique based on a thorough understanding of current farming systems.

- For each technique, identify those areas where costs or performance changes will be associated with the introduction of that technique.

- In all cases, only those costs directly associated with the techniques should be considered.

- As the assessment of costs is at farm level, any grants that are available should be deducted from expenditure.

The category that techniques fall into will determine the physical units that are used to define the population or quantities of manure, and from the basis of subsequent calculations. The relationship can be seen from the following table.

Table 1. ‘Units’ Used for Assessing Costs

| Category | ‘Units’/Year | Details |
| --- | --- | --- |
| Feed and housing | Per head Per kg NH3 Per kg pig produced | Building capacity |
| Manure and slurry storage | m3 or tonnes Per kg NH3 Per kg pig produced | Liquid slurry (including dilution) and solid manure (including bedding) |
| Manure and slurry treatment |  |  |
| Manure and slurry application |  |  |

Unit costs should be calculated according to the general approach described below:

- Current cost should be used for all calculations

- Capital expenditure, after deducting any grants, should be annualised over the economic life of the investment.

- Annual running costs should be added to the annualised cost of capital

- Changes in performance have a cost and should be taken into account

- This total sum is divided by the annual throughput to determine the ‘unit cost’

Annual cost is expressed by the ‘units’ shown in Table 1.

For pig production, costs are also expressed as € per t pig produced with the next assumptions for the calculations:

- Equivalences:

  - 1 sow productive place produces 20.00 pigs marketed/year

  - 1 gestating place produces 26.60 pigs marketed/year

  - 1 lactating place produces 80.00 pigs marketed/year

  - 1 nursery place produces 5.79 pigs marketed/year

  - 1 grower place produces 2.94 pigs marketed/year

  - 1 pig marketed produces 1.25 m3 of slurry

- Pig marketed = 100 kg body weight

## Basis of the annualisation of capital expenditure

The calculation of the annual cost of capital items has been based on the following criteria:

Were:   C = Capital cost

r = Interest rate

n = Write off period (years)

Based on an amortisation rate of 5% which is the current rate of interest commonly incurred by farmers seeking medium term loans.

Write off periods according to investment type as set out in Table 2.

Table 2.  Capital write off periods

| Category | Write off period Years | Interest rate at 5% |
| --- | --- | --- |
| New buildings | 20 | 0.080 |
| Equipment installed in buildings | 10 | 0.130 |
| Machinery (depending on type) |  |  |
| either | 7 | 0.173 |
| or | 5 | 0.231 |

These figures reflect the economic life over which the investment should be considered rather than operational life. Annual cost for repairs is based in the estimations carry out by Nix, 2003.

# Results

## Feeding strategies

Next table shows cost of feeding strategies to grower and finisher pigs.

Table 3.  Effective unit cost for feeding strategies

| Technique | Extra cost (€/place) | Extra cost (€/kg pig) | % red | Ammonia reduction (kg/place) | Extra cost (€/kg NH3) |
| --- | --- | --- | --- | --- | --- |
| Phased feeding | 1.52 | 0.0052 | 10 | 0.32 | 4.8 |
| Low protein diet with unfavourable market conditions | 1.61 | 0.0053 | 30 | 0.95 | 1.7 |
| Low protein diet with favourable market conditions | -1.92 | -0.0064 | 30 | 0.95 | -2.0 |

In GAINS, cost for feeding strategies in Spain is 6.7 €/kg NH3.

## Housing strategies

Next table shows cost of stable adaptation strategies to different phases of pig production.

Table 4.  Effective unit cost for housing strategies

| Technique | Phase | Extra cost (€/place) | Extra cost (€/kg pig) | % red | Ammonia reduction (kg/place) | Extra cost (€/kg NH3) |
| --- | --- | --- | --- | --- | --- | --- |
| Partial slat and reduced pit. New building | Gestating sows | 5.68 | 0.0021 | 35 | 0.95 | 6.0 |
| Partial slat and reduced pit. Existing building | Gestating sows | 6.83 | 0.003 | 35 | 0.95 | 7.2 |
| Littered system. N.B. | Gestating sows | 55.35 | 0.0208 | 14 | 0.38 | 146.4 |
| Littered system. E.B. | Gestating sows | 80.45 | 0.0302 | 14 | 0.38 | 212.8 |
| Frequent manure removal | Gestating sows | 0 | 0 | 25 | 0.68 | 0.0 |
| Combination water-manure channel. N.B. | Lactating sows | 3.29 | 0.0004 | 52 | 1.94 | 1.7 |
| Combination water-manure channel. E.B. | Lactating sows | 16.74 | 0.0021 | 52 | 1.94 | 8.6 |
| Manure pan underneath. N.B | Lactating sows | 17.52 | 0.0022 | 32 | 1.19 | 14.7 |
| Manure pan underneath. E.B | Lactating sows | 30.98 | 0.0039 | 32 | 1.19 | 26.0 |
| Manure channel with sloped floor. N.B. | Weaners | 0.23 | 0.0004 | 60 | 0.43 | 0.5 |
| Manure channel with sloped floor. E.B. | Weaners | 2.67 | 0.0046 | 60 | 0.43 | 6.2 |
| Partial slat. N.B. | Weaners | 0.88 | 0.001 | 25 | 0.18 | 4.9 |
| Partial slat. E.B. | Weaners | 2.25 | 0.0026 | 25 | 0.18 | 12.5 |
| Frequent manure removal | Weaners | 0 | 0 | 25 | 0.18 | 0.0 |
| Partial slat. N.B. | Growers-finishers | 0 | 0 | 30 | 0.95 | 0.0 |
| Partial slat. E.B. | Growers-finishers | 3.61 | 0.0123 | 30 | 0.95 | 3.8 |
| Manure channel with sloped floor. N.B. | Growers-finishers | 0.73 | 0.0263 | 10 | 0.32 | 2.3 |
| Manure channel with sloped floor. E.B. | Growers-finishers | 6.45 | 0.0219 | 10 | 0.32 | 20.4 |
| Littered system. N.B. | Growers-finishers | 25.72 | 0.0875 | 20 | 0.63 | 40.7 |
| Littered system. E.B. | Growers-finishers | 42.07 | 0.1431 | 20 | 0.63 | 66.6 |
| Frequent manure removal | Growers-finishers | 0 | 0 | 30 | 0.95 | 0.0 |

In GAINS, cost for housing strategies in Spain is 27.6  €/kg NH3.

## Storage strategies

Next table shows cost of storage strategies to an on site farm.

Table 5.  Effective unit cost for storage strategies

| Technique | Extra cost (€/m3) | Extra cost (€/kg pig) | % red | Ammonia reduction (kg/place) | Extra cost (€/kg NH3) |
| --- | --- | --- | --- | --- | --- |
| Natural crust | 0 | 0 | 28 | 0.15 | 0.0 |
| Floating cover | 2.3 | 0.0288 | 70 | 0.75 | 3.1 |

In GAINS, cost for storage strategies in Spain is 3.0 - 3.6 €/kg NH3.

## Land application strategies

Next table shows cost of land application strategies to an on site farm.

Table 6.  Effective unit cost for land application strategies

| Technique | Extra cost (€/m3) | Extra cost (€/kg pig) | % red | Ammonia reduction (kg/place) | Extra cost (€/kg NH3) |
| --- | --- | --- | --- | --- | --- |
| Trailing shoe | 1.41 | 0.0176 | 50 | 0.27 | 5.1 |
| Band spreader | 1.21 | 0.0151 | 40 | 0.22 | 5.5 |
| Incorporation | 0.61 | 0.0076 | 30 | 0.16 | 3.7 |

In GAINS, cost for land application strategies in Spain is 5.7 – 12.1 €/kg NH3.

# Discussion

## Economics of pig sector in Spain

With the aim of consider costs in all productive phases, the study is carried out in an on site farm.

Cost production in the pig sector for this production type in Spain in last years is shown in the next table.

Table 7.  Cost of production in Spain

|  | Average costs per pig slaughtered with 100 kg |
| --- | --- |
|  | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 |
|  | € | % | € | % | € | % | € | % | € | % | € | % | € | % |
| Food | 51.10 | 71.14 | 54.10 | 73.14 | 59.4 | 62.4 | 61.6 | 62.5 | 73.3 | 65.2 | 82.1 | 67.7 | 68.1 | 64.4 |
| Fixed costs | 14.90 | 20.74 | 14.80 | 20.01 | 28.0 | 29.4 | 29.1 | 29.5 | 30.1 | 26.8 | 30.0 | 24.7 | 29.1 | 27.5 |
| Insemination | 0.95 | 1.32 | 0.91 | 1.23 | 0.9 | 0.9 | 0.9 | 0.9 | 1.1 | 1.0 | 1.2 | 1.0 | 1.0 | 0.9 |
| Renovation sows | 1.88 | 2.62 | 1.26 | 1.70 | 1.6 | 1.7 | 2.0 | 2.0 | 2.0 | 1.8 | 2.1 | 1.7 | 2.0 | 1.9 |
| Medication | 3.00 | 4.18 | 2.90 | 3.92 | 5.3 | 5.6 | 5.0 | 5.1 | 5.8 | 5.2 | 5.9 | 4.9 | 5.6 | 5.3 |
| Total cost (pig 100 kg) | 95.80 | 100 | 100.3 | 100 | 95.2 | 100 | 98.6 | 100 | 112.4 | 100 | 121,3 | 100 | 105,8 | 100 |
| Total cost (per kg) | 0.958 | 1.003 | 0.952 | 0.986 | 1.124 | 1.213 | 1.058 |

In the next graphic, cost, price and margin before tax are shown.

Graph 1.  Economics of pig sector in Spain. 2003-2009

Profitability margins are narrow and it obtains negative values in several periods.

As an example, in an on site pig farm with 100 sows, what produces 20 pigs marketed (100 kg) per sow per year, the average annual profitability in the studied period (2003-2009) was 9880 € each year (0,0494 €/kg pig).

## Ammonia abatement cost

Annex IX includes measures for the control of emissions of ammonia from agricultural sources. For each phase, strategies recommended are open in three options (A, B or C). Option A is the most restrictive an option C is the less restrictive.

The possibilities are:

Table 8.  Ammonia abatement possibilities under Spanish conditions for pig sector

|  | Option A | Option B | Option C |
| --- | --- | --- | --- |
| Feeding | Low protein diet | Phased feeding | Phased feeding |
| Housing | Partial slat Frequent manure removal Manure pan of manure channel | Partial slat Frequent manure removal Manure pan of manure channel | Partial slat Frequent manure removal Manure pan of manure channel |
| Storage | Floating cover | Floating cover | Floating cover |
| Spreading | Trailing shoe | Incorporation | Incorporation |

In the next table, ammonia abatement cost is summarized to each option, for a full cycle (feeding + housing + storage + spreading) in an on site pig farms.

Table 9.  Ammonia abatement extracost for different options

|  | Feeding strategies | Housing | Storage | Spreading | Total (€/kg pig) |
| --- | --- | --- | --- | --- | --- |
| Option A | 0.0053 | 0.0263 | 0.0288 | 0.0176 | 0.0780 |
| Option B | 0.0052 | 0.0123 | 0.0288 | 0.0076 | 0.0539 |
| Option C | 0.0052 | 0 | 0.0288 | 0.0076 | 0.0416 |

The farm profitability with the three options is:

Table 10.  Influence of different options in farm profitability

|  | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | Average 03-07 | Total (€/farm*/year) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Option A (€/kg pig) | -0.086 | 0.009 | 0.070 | 0.136 | -0.162 | -0.151 | -0.036 | -0.0314 | -6286 |
| Option B (€/kg pig) | -0.062 | 0.033 | 0.094 | 0.160 | -0.138 | -0.127 | -0.012 | -0.0073 | -1466 |
| Option C (€/kg pig) | -0.050 | 0.045 | 0.106 | 0.172 | -0.126 | -0.115 | 0.001 | 0.0050 | 994 |

*A 100 sows-on site farm, with 20 pigs (100 kg) per sow per year.

## Ammonia emissions in the whole cycle

In pig production, ammonia is emitted along a chain and the measures introduced at the beginning influence at emission in the other links.

Also, emissions are not similar in all compartments. In Spanish pig production, ammonia emission distribution is shown in next graph.

Graphs 2.  Ammonia emission in pig production (for an on site farm)

It is necessary to select the actuation point in the application of abatement techniques. For example, housing strategies in gestating, lactating or weaners rooms increase production costs significantly and the reduction in ammonia emissions is negligible. To introduce partial slat in existing building in an on site farm (100 sows) for these phases has a cost of 1960 €/year. Total ammonia emission reduction is 2.3%.

# Conclusions

- Results obtained with cost methodology BREF, 2003 adapted by Spanish Working Group are in range with GAINS data. We can conclude that both systems are equivalent.

- Some techniques can be rejected by their high cost, as littered systems.

- Economic resources to improve environmental conditions in pig farm are limited because the small profitability of Spanish pig sector. This situation is transferable to the livestock sector in Europe.

- If Administration demands measures for the control of emissions in all compartments and for all animal phases, profitability will disappear. Ammonia emissions will not reduce, but will transfer to other world areas with environmental legislation less restrictive.

- Because of this resource limitation, it is necessary to optimise the efforts for the minimisation of ammonia emissions, promoting measures that reduce emissions in origin and avoiding that those preliminary efforts get lost at the end of the chain.

- As an example, in Spanish pig sector measures should be applied, to optimise resources, in housing (growers-finisher phase) and in land application.

Graphs 3.  Ammonia emission distribution in pig farms

- Nutritional strategies are the most effective techniques because it reduces nitrogen excretion in origin, therefore, ammonia emissions along whole chain. For a growers-finishers pig farm, nutritional strategies that reduce nitrogen excretion (low protein diet), reduce ammonia emissions in all chain a 25%. Average cost is between -0.0064 (save) and 0.0053 €/place and year.

- Land application strategies have a double benefit because it reduces ammonia emission in an important phase (31% total emissions) and allows to make use of nitrogen as fertiliser, with the consequent save in fertilization.

- It is indispensable that the environmental demands do not finish with the profitability of livestock sector. Because of this, to calculate total cost of techniques implemented is so important as to know the total environmental benefit.

- Actual proposal of measures for the control of emissions of ammonia from agricultural sources will finish with the profitability of affected farms.

# References

European Commission, 2003. Integrated Pollution Prevention and Control. Reference Document on Best Available Techniques for Intensive Rearing of Poultry and Pigs (BREF).

Nix, J. 2003. Farm Management Pocketbook. Imperial College at Wye. 33rd edition.

# Acknowledgements

This work is part of a project funded by the Spanish Ministry of the Environment and Rural and Marine Affairs. We also thank Martin Ryan (Natural England) for this help in cost calculation and methodology explanation.